## Slide 1
FINAL PRESENTATION Iowa State University
04/22/2024

## Slide 2: Team Introductions
Michael T - Branstad
Jack Smith
Saul Huntley-Ayala
Ashley Althaus
Austin Nolley
Dr. Brian Steward
Dr. Saxon Ryan

## Slide 3: Overview
Vehicle Construction
  Component Design
Final Vehicle
Hydraulic & Pneumatic Circuits
Bike Changes & Improvements
Electronic Controls & Instrumentation
Lessons Learned

## Slide 4: Failure Investigation
Last year we suspected one or more components failed during the competition.
Micro Pump, 2.8cc motor, reservoir design

## Slide 5: Goals
Minimize Pressure Losses
  Change size and orientation of solenoids
Maximize Direct Drive Efficiency
  Resize human input pump
  Replace the large chain reduction with a gear box for better packaging.
Finish on the Podium in the Competition
  Finish first in efficiency test
  Finish in top three in regen and sprint test

## Slide 6: Design Choices
Design of new frame
  Use extruded aluminum T-Slot channel framing | 80/20 brand
  Enhanced rigidity where it was needed to maintain chain alignment
  Redesign the fluid revisor and reintroduce a seat to the frame
  Transfer several components from old frame to new frame
Design of New Circuit
  Use of 4 2/2 normally closed DCV's in parallel
  Increase available flow rate to reduce pressure drop
Design of New Gear Box
  1:19.75 Gearbox ratio
  1:82 Overall ratio

## Slide 7: Testing
Disassembled 0.3cc/rev micro pump
Tested micro pump with the old reservoir
Straight lined directly connected to 2.8cc/rev motor

## Slide 8: Vehicle Construction
Construction in progress
New Frame Design
Members made of 45x90 and 45x45 extruded aluminum
Makes for easy placement and chain alignment

## Slide 9: Designed Components
80-20 Bracket
Axle Spacer
Back Tire Bracket
Bike Sprocket Adapter

## Slide 10: Designed Components
Gearbox – Final Side 1/8th" thick steel. Dimensions are 6.75 x 9 inches
Pump Mount
Fluid Reservoir and Bracket.
(Initial thought)
Fluid Reservoir DWG

## Slide 11: Current Vehicle State

## Slide 12: Previous Hydraulic Circuit

## Slide 13: Current Hydraulic Circuit
Pedal Circuit
Accumulator and Regen Circuit
Improvements: One 4/3 DVC replaced with 4 2/2 DCV in parallel
Manual valve taken out of circuit
Added hand pump

## Slide 14: Pedal Power

## Slide 15: Accumulator Pressurization

## Slide 16: Accumulator Power

## Slide 17: Regen Power

## Slide 18: Pneumatic Circuit

## Slide 19: Electronics
2 – 12-volt interstate batteries (total 24 volt) powering four solenoids above the manifold connected by switches in the front of the bike.
Our original plan was to utilize the controller from previous team designs but have faced issues with software and time constraints. The use of the switches achieved the same goal with a simpler approach.

## Slide 20: Hardware Selection

## Slide 21: Lessons Learned
Long lead times for components
Chain alignment and hardware must be precise
Utilize knowledge of industry professionals
  Establishing mentors
  Fostering relationships
Setting deadlines is essential
  Planned worktimes and meetings
Communication with group members and mentors is important

## Slide 22
Thank you!