## Slide 1
FINAL PRESENTATION Michigan Technological Univ.
Advisor: Dr. Dave Wanless
4/12/2024
University Image Logo

## Slide 2: Team Introduction
Isaac Steers
Collin Little
Luke Hensley
Tate Newlin
Cheyenne Goff
Notes: All

## Slide 3: Key Design Choices
Pump Action Pedals
Dual Rim Pulley System
Motor Mount
Accumulator attachment
Relief/control valve attachment
Tensioner

## Slide 4: Pedal Design
Small piston 3.8 inches from axis of rotation
Pedals are 28” long from axis
Aluminum square stock for lightness
Steel wire on a pulley for pedal return

## Slide 5: Dual Rim Pulley Design
Two 26” rims tig welded together
0.35” thick belt to motor
Position of motor based off location of the belt rim

## Slide 6: Motor Design
Casappa gear motor (0.683 in3/rev at 100% efficiency, 26.25 in. lbs, 115.86 rpm, 0.3805 gpm)
Pulley attached to Motor that drives the belt (3in pulley)
Welded Motor Mount and custom bracket

## Slide 7: Cylinder Design
Cylindrical pistons are used to utilize leverage and linear motion
Different size pistons used as gearing
Electronic control gear selector
Stroke is 2.5” for small and 5” for large pistons
Displacement is .85 in^3 and 1.7 in^3 for small and large respectively
Cylinders manufactured by Jarp Industries

## Slide 8: Electronic system
Envision PV500 screen (Iowa Fluid Power Supplied)
Envision MC2 controller
Barksdale Bps3000 pressure sensor
Balluff BSP pressure sensor
Two Milwaukee M18 batteries
Custom Deutsch connector wiring harness

## Slide 9: Electronic Programming
An touchscreen design solved problems from previous years (manual valves)
Powervision used to program the screen
CoDeSys used to program the controller
Different buttons for specific modes
Separate logic for gears and modes

## Slide 10: Tensioner Design
Chamfered nylon
welded threaded rods to tension
Attached to Motor Mount (weld)

## Slide 11: Valve Selection
Sun Hydraulics cartridge valves and manifolds
14 V solenoid actuation

## Slide 12: Valve Mount Design
Two manifold banks
Threaded rods through manifolds
Nuts clamp the manifolds to the frame
Attached to a back plate or the accumulator mounts

## Slide 13: Accumulator Design
Bent threaded rod attached to 1x1 aluminum square tubing for mounting
2 accumulators (1.89 liter & .945 liter)

## Slide 14: Vehicle Construction/Final Vehicle
Primarily done on our own, with tools and materials from the MTU MMET Shop
Original plans were much different from the final outcome

## Slide 15: Vehicle Testing
Initial testing was done to check for piston function
Piston to motor fluid movement check
Connection and hose failures
  Calculations and earlier tests show it will work

## Slide 16
Rigged Schematic

## Slide 17: Competition Schematic

## Slide 18: Lessons Learned
Start designing and planning sooner
Go through hose and valve connections early
How to deal with last-minute issues
Small errors can change an entire design
Proper fittings for circuit & components

## Slide 19: Thank You
Josh Scarbrough IFP
Joe Jackan from Jarp Industries
Ernie Parker
Dave Wanless
MTU MET department